## Slide 1: ELEC6098 Electronic Commerce & Mobile Commerce
Dr. Wilton Fok

## Slide 2: Enabling Technology: Location Base Service

## Slide 3: Enabling Technology: Location Base Service
Cellular radio network is the foundation for location base services
GSM is a cellular network
   mobile phones connect to it by searching for cells in the immediate vicinity.

## Slide 4: GSM
GSM (Global System for Mobile Communications is/was the most popular standard for mobile telephony systems in the world.
GSM is considered a 2G mobile phone system.
It facilitates the wide-spread implementation of data communication applications into the system.
Advantages
  Roaming
  Switch carriers without replacing phones
  Support SMS
  Support SIM Card
  Support a worldwide emergency telephone number feature 112

## Slide 5: SIM Card in GSM
SIM Card = Subscriber Identity Module
A detachable smart card containing the user's subscription information and phone book.
This allows the user to retain his or her information after switching handsets.
User can also change operators while retaining the handset simply by changing the SIM.
Some operators will block this by allowing the phone to use only a single SIM
  SIM locking

## Slide 6: SIM locking
Some mobile phone operators restrict handsets that they sell for use with their own network.
Implemented by a software feature of the phone.
  Because the purchase price of the mobile phone to the consumer is typically subsidized with revenue from subscriptions, operators must recoup this investment before a subscriber terminates service.
Ways to unlock the SIM
  Contact the provider to remove the lock for a fee,
  utilize private services to remove the Lock, or
  Make use of free or fee-based software and websites to unlock the handset themselves.
  More shown on youtube

## Slide 7: GSM improvement
1997 Introduce of General Packet Radio Service (GPRS)
1999 Introduce higher speed data transmission using Enhanced Data Rates for GSM Evolution (EDGE).

## Slide 8: Network structure
The structure of a GSM network:
  Base Station Subsystem
    base stations and their controllers
  Network and Switching Subsystem
    part of the network most similar to a fixed network). This is sometimes also just called the core network.
  GPRS Core Network
    the optional part which allows packet based Internet connections
  Operations support system (OSS)
    for maintenance of the network.

## Slide 9: Network structure
Base Station Subsystem
Network and Switching Subsystem
GPRS Core Network
Operations support system (OSS)

## Slide 10: Cell sizes and coverage
There are 5 different cell sizes in a GSM network
  Macro,
  Micro,
  Pico,
  Femto and
  Umbrella cells.

## Slide 11: Cell sizes and coverage
The coverage area of each cell varies according to the implementation environment.
  Macro cells
    Cells where the base station antenna is installed on a mast or a building above average roof top level.
  Micro cells
    Those antenna height is under average roof top level; they are typically used in urban areas.

## Slide 12: Cell sizes and coverage
  Picocells
    Small cells whose coverage diameter is a few dozen metres; they are mainly used indoors.
  Femtocells
    Cells designed for use in residential or small business environments and connect to the service provider’s network via a broadband internet connection.
  Umbrella cells
    Used to cover shadowed regions of smaller cells and fill in gaps in coverage between those cells.
Femtocells

## Slide 13: Cell sizes and coverage
Cell horizontal radius varies depending on:
    antenna height,
    antenna gain
  propagation conditions from a 300m -35km

## Slide 14: Cell sizes and coverage
Indoor coverage is also supported by
  indoor picocell base station, or
  an indoor repeater with distributed indoor antennas fed through power splitters,
  to deliver the radio signals from an antenna outdoors to the separate indoor distributed antenna system.
  E.g. In shopping centers or airports.

## Slide 15: Cellular Network
Use multiple low-power transmitters (100 W or less)
Areas divided into cells
  Each served by its own antenna
  Served by base station consisting of transmitter, receiver, and control unit
  Band of frequencies allocated
  Cells set up such that antennas of all neighbors are equidistant (hexagonal pattern)
910MHz
915MHz
920MHz

## Slide 16: Cell Format

## Slide 17: Frequency Reuse
Adjacent cells assigned different
  frequencies to avoid interference or crosstalk
Objective is to reuse frequency in nearby cells
  10 to 50 frequencies assigned to each cell
  Transmission power controlled to limit power at that frequency escaping to adjacent cells
  The issue is to determine how many cells must intervene between two cells using the frequency
910MHz
915MHz
920MHz
910MHz
noise

## Slide 18: Frequency Reuse
N=1,3,4,7,9,12,13,16,19 ..

## Slide 19: Frequency Reuse
Larger N
  Longer distance between cell with the same frequency
  Less co-channel interference
Co-channel
interference

## Slide 20: Frequency Reuse
Power is inversely proportional to Distance (Inverse square law)
 Signal to Noise is proportional to N2

## Slide 21: Approaches to Cope with Increasing Capacity
Adding new channels
Frequency borrowing
  frequencies are taken from adjacent cells by congested cells
Cell splitting
  cells in areas of high usage can be split into smaller cells
Cell sectoring
  cells are divided into a number of wedge-shaped sectors, each with their own set of channels
Microcells
  antennas move to buildings, hills, and lamp posts
Cell Splitting

## Slide 22: Capacity vs Accuracy
When N is large
  Less co-channel interference
  Stronger signal to noise ratio
  Smaller cell-site
  More accurate in location estimation
But require more frequency resources
910MHz
915MHz
920MHz
910MHz
Co-channel
interference

## Slide 23: Methodologies for location estimation
Time of arrival (TOA)
  Time predict distance
  3 distance data locate a point
Angle of arrival (AOA)
  3 angles location a point

## Slide 24: Methodologies for location estimation
Time difference of arrival (TDOA)
  If it can only access two Base-station, distance between base-stations provide the 3rd information

## Slide 25: Methodologies for location estimation
Enhanced observed time difference (EOTD)
Cell global identification (CGI) and Timing advance (TA)
Signal strength (SS)
Global Positioning System (GPS)
Control Plane Locating

## Slide 26: Methodologies for location estimation
Control plane locating
  Service provider gets the location based on the radio signal delay of the closest cell-phone towers (for phones without GPS features) which can be quite slow as it uses the 'voice control' channel.
  Some primitive LBS services use a single base station, with a 'radius' of inaccuracy, to determine a phone's location. This technique was the basis of the E-911 mandate and is still used to locate cell phones as a safety measure.
More details
  http://www.hkwtia.org/

## Slide 27: Error of location base estimation
Scattering
Shadowing
Reflection
Diffraction
Co-channel interference

## Slide 28: What’s is Location Base Service
A location-based service (LBS) is an information and entertainment service, accessible with mobile devices through the mobile network and utilizing the ability to make use of the geographical position of the mobile device
E.g. identify a location of a person or object such as discovering the nearest banking cash machine or the whereabouts of a friend or employee.

## Slide 29: Basic operation modes of LBS
Pull
  The customer initiates mobile positioning measurement at the same time when one requests for a service
Push
  The request for service (and hence mobile positioning) is not technically made by the customer but by the service provider
Tracking
  Someone (person or service) asks for a location of the mobile terminal (Person, vehicle, fleet etc.)

## Slide 30: Class discussions: What are the applications of LBS?

## Slide 31: Applications of Location base Services
Emergency services
Mobile advertising
Location sensitive billing
Fraud protection
Asset tracking
Fleet management
Intelligent transportation systems
Mobile yellow pages
parcel tracking and vehicle tracking services
Location base coupons or advertising
personalized weather services and
location-based games
Requesting the nearest business or service, such as an ATM or restaurant
Locating people on a map displayed on the mobile phone
Receiving alerts, such as notification of a sale on gas or warning of a traffic jam

## Slide 32: Applications of Location base Services
Resource tracking with dynamic distribution.
  Taxis, service people, rental equipment, doctors, fleet scheduling.
Resource tracking.
  Objects without privacy controls, using passive sensors or RF tags, such as packages and train boxcars.
Finding someone or something.
  Person by skill (doctor), business directory, navigation, weather, traffic, room schedules, stolen phone, emergency calls. Targeted advertising, buddy list, common profile matching (dating)

## Slide 33: Values of LBS
Use as a filter
  to restrict results of search that are close enough to the customers’ location
Use as a pointer
  to show the location of the customers as a dot on a map in tracking services
Use as a definer/launcher for “area alarm
  i.e. to launch a pre-defined activity (e.g. send a MSMS) with customer enters/leaves a certain area

## Slide 34: CNN news on location Base service
http://www.youtube.com/watch?v=NwuW5BCaj-I

## Slide 35: Class discussions: What are the issues/problems of LBS?

## Slide 36: What are the issues/problems of LBS?
Privacy
Accuracy
Coverage
Useless information (Garbage information)
Information overload

## Slide 37: Major issues faced by LBS
Accuracy of location
  Mobile network was primarily built for communication, not positioning
  If location data is not accuracy, the information is not useful (Garbage in, Garbage out)
  Limiting choice of service

## Slide 38: Major issues faced by LBS
Investment vs penetration
  Extraction of network measurement for position calculation remains a difficult and expensive task
  Network base solution offers a full-base penetration  but large investment
  Terminal based solution is relatively less expansive but largely limits penetration

## Slide 39: Major issues faced by LBS
Business Model (Willingness to pay)
  Consumer market: position information in most cases are just “nice-to-have”. There is no killer application
  Enterprise users are more willing to pay a higher fee
Inter-operability between operators
  Cross border continuity
  Difference in positioning accuracy
  Commercial models in roaming

## Slide 40: Major issues faced by LBS
Privacy
  Opt-in/ Opt-out policy
  Applications development/service provider
  Dilemma of In-house/out-source development
    Outsourcing the service/development can reduce the cost of operation. But the operator’s network data are very sensitive and involve privacy issues.

## Slide 41: Q&A

## Slide 42: Enabling Technology: QR CODE

## Slide 43: Barcode vs QR Code
Barcode
  a code consisting of a group of printed and variously patterned bars and spaces and sometimes numerals that is designed to be scanned and read into computer memory and that contains information (as identification) about the object it labels.
QR Code
  a matrix barcode (or two-dimensional code), readable by QR scanners, mobile phones with a camera, and smartphones.

## Slide 44: Different Codes
Code 39
Defines 43 Characters.
Typically used in non-retail areas.
Arguably the simplest barcode.

## Slide 45: Different Codes
Code 128
Defines the entire 128 ASCII character set.
Typically used in shipping/retail.

## Slide 46: How does a scanner/smartphone interpret a barcode?
Each barcode is interpreted similarly and yet also slightly differently as well.
Barcodes also happen to be less complex that QR Codes.
Barcodes can use scanners, whereas QR Codes require something else (i.e smartphones, computer, game machines)

## Slide 47: Barcodes
Barcode scanners are made of 3 different parts: an illuminator, a convertor, and a decoder.
The illuminator shoots out a line of light (typically red) at the barcode.
Light will reflect from the barcode (from anywhere that is not black) in the form of a wave.
The convertor converts the wave into a readable form for the device.
Decoder reads the converted information.
Light from Scanner
Barcode
Light Reflection

## Slide 48: QR Codes
Certain applications on a smart phone / portable gaming device can scan QR codes.
Instead of bouncing off an image via light, QR Codes are interpreted from a picture skipping the light wave process.

## Slide 49: QR Code

## Slide 50: QR Codes
Interpretation of the code is that excluding the no zones, each black module is a 1 bit and a white one is a 0 bit.
0
1

## Slide 51: QR Code
QR codes currently support alphanumeric data capacities of up to about 400 bytes and binary capacities of up to about 270 bytes,
Handsets requirement:
  macro focus
  resolutions of several megapixels
Fig. QR codes encoding alphanumeric data “a123456789a12…” of length (a) 40, (b) 100, (c) 200 characters

## Slide 52: QR Code
The capacity (when read by a typical camera phone without macro focus, but with resolution of one megapixel or more)
  close to 100 bytes of alphanumeric characters or
  70 bytes of binary data
Error control:
  The QR symbology supports error correction using the Reed-Solomon method.
  There are four levels of error correction, selectable according to the operating environment.
  The capability ranges from correcting about 7% of the data in a code, to about 30%.

## Slide 53: QR Codes
Error Correction
This allows other images to be placed into the code without any issues.
Still works!

## Slide 54: Algorithm of QR Code (not exam)
http://en.wikipedia.org/wiki/QR_Code

## Slide 55: Create a QR Code
http://www.swetake.com/qr/qr1_en.html

## Slide 56: QR Code generator
http://qrcode.kaywa.com/

## Slide 57: QR Code generator
http://zxing.appspot.com/generator/

## Slide 58: What are the benefits of QR Code?

## Slide 59: Benefits of QR Code
Benefits of QR Code for:
  consumers,
  marketing,
  mobile industries
  Wireless Operators
  Handset Manufacturers
  Application and Service Providers

## Slide 60: Benefits to Consumers
Reading a mobile code is faster and more convenient
  than transcribing data such as URLs, telephone numbers and SMS messages into handsets.
Less error-prone
   error correction in the codes guarantees against entering incorrect data.
No need to navigate to the appropriate application on their handset
  It is implicit in the type of data in the code. \
Especially helpful with respect to web browsers
  users find difficult to locate and operate on their handsets.

## Slide 61: Benefits to Marketer
Encourage users to participate in promotional campaigns
  compared to manual transcription of URLs etc., mobile codes increase response rates.
Enable print advertising
  QR code can be placed in media formats, markets and physical locations, marketers can measure which placements were more effective than others.

## Slide 62: Benefits to Wireless Operators
In the past, SMS did not scale in usability, mainly ringtone downloads only
QR codes promote mobile internet as more connections are made direct from advertisement to web.
Increase operator’s ARPUs (Average Revenue Per User) through more and more rewarding internet connections.
ARUP of Orange Source:
http://wiki.mbalib.com/w/index.php?title=Orange%E5%85%AC%E5%8F%B8&variant=zh-tw

## Slide 63: Benefits to Wireless Operators
ARUP and ratio of Data Service

## Slide 64: Benefits to Wireless Operators
Operators can help drive the reach and scale of the mobile code scanning opportunities by ensuring that scanning clients and applications are pre-installed in the mobile devices.

## Slide 65: Benefits to Wireless Operators
Operators may be able to associate such user inquiries with the user’s preferences based on his/her subscription profile
Selling customer profiles to advertisers creates a new stream of revenue.
Target marketing with deeper profile data of prospective customers.
Privacy concerns need to be considered as applicable.

## Slide 66: Handset Manufacturers
Feedback from mobile code adoption in Japan suggests that, once established in the market, mobile code readers become a “must have”.
Handset companies will want to provide a compelling reason to upgrade to their mobile code-enabled terminals.

## Slide 67: Application and Service Providers
Provides the new internet experience, impact on mobile content and service provision.
Innovate new user interaction with mobile codes, and in new mobile code support services.
Both application and service sectors have the opportunity for significant growth, perhaps enabling different actors in the value chain

## Slide 68: References
http://en.wikipedia.org/wiki/QR_Code
Open Mobile Alliance - White Paper on Mobile Codes
    http://www.openmobilealliance.org/Technical/release_program/docs/MobileCodes/V1_0-20081024-A/OMA-WP-MobileCodes-20081024-A.pdf
UID Solutions - UID Products and Services for US Military Contractors and DoD. Barcode History Timeline. Retrieved from http://www.uidsolutions.com/barcodetimeline.html
Qr readers. (n.d.). Barcode Technology Timeline. Retrieved from http://www.qrreaders.net/articles/barcode-technology-timeline.html
What Is A QR Code And How Does It Work?. http://www.youthedesigner.com/2011/09/29/what-is-a-qr-code-and-how-does-it-work/.
How Barcode Scanners Work. http://www.carolinabarcode.com/how-barcode-scanners-work-a-69.html.
Information technology — Automatic identification and data capture techniques — Bar code symbology — QR Code. http://raidenii.net/files/datasheets/misc/qr_code.pdf.